| ; TSB ; . | Model; Cee'd [ED](); . |
| --- | --- |
| Group; Emission Control System(13); . |
| TSB No.; KFE08-13-V040-ED; . |
| Subject; . OXYGEN SENSOR INSPECTION & BURN OUT PROCEDURE (CEE’D 2.0 L BETA ENGINE); . | Published; 5/22/2008; . |
| TSB Type; Field Fix; . |
| Area & Distributor; ; . |

1. Description

■ Symptom/Condition

Customer on cee’d 2.0 L Beta engine vehicle might experience the engine warning light on, which DTC

P0139, P0133 or P0170 might be affected.

■ Cause

Due to the water contamination of the oxygen sensor or leaking of exhaust system.

■ Countermeasure/Remedy

Conduct burn out procedure and check if DTCs related to the exhaust system and the oxygen sensor are

detected with Scan tool according to the Service Procedure below.

2. Applicable Vehicles;

■  Model : cee’d (ED),

■  Applicable vehicle production date range: Produced from Job #1 to Feb. 15, 2008 (U5YFF24328L110155)

■  Applicable VIN: Produced from Job #1 to U5YFF24328L110155

■  Area : Europe

3. Operation Code And Time

■ WARRANTY INFORMATION

| OP CODE | OP NAME | OP TIME | NATURE | CAUSE |
| --- | --- | --- | --- | --- |
| 39210F04 | OXYGEN SENSOR BURN-OUT AND DTC CHECK | 0.3 M/H | *N69 | **C99 |

*N69 Warning lights on

**C99 Other

4. Service Procedure

| Note) Before conducting this procedure, verify that the vehicle is affected one by identifying the VIN. |
| --- |
| 1) Disconnect the oxygen sensor wiring connector (A). |  |
| 2) Shift gear into P or N position and apply the parking brake. 3) Heat up the engine at 3000rpm for 10 min. 4) Re-connect the oxygen sensor wiring connector (C). 5) Erase DTC caused by disconnection of oxygen Sensor with Scan-tool. 6) Re-check if there are DTCs related to oxygen sensor and exhaust system. Note) If any DTC related to oxygen sensor and exhaust system, repair condition according to the applicable DTC troubleshooting manual. But, if no DTC, complete this procedure. |