| ; TSB ; . | Model; Cee'd [ED](all); . |
| --- | --- |
| Group; Топливная система(14); . |
| TSB No.; KFE08-14-P030-ED; . |
| Subject; . ECM UPGRADE - HESITATION WHEN ACCELERATING; . | Published; 1/28/2008; . |
| Area & Distributor; West Europe, East Europe; . |

1. Description

This bulletin provides information regarding ECM software upgrade for cee'd (ED) U-1.6L VGT diesel vehicles which may hesitate when accelerating while driving, to improve control of the amount of air in the intake path by modifying the EGR and boost pressure related governing factors.

2. Applicable Vehicles;

■ Model: cee'd (ED) vehicles with U-1.6L VGT diesel engines

■ Applicable vehicle production date range: From start of production

NOTE)

- Verify the version of ECM ROM ID before attempting to upgrade the vehicle's ECM software.

Refer to the ROM ID Information Table below.

■ Area: Europe

3. Parts Information;

■ ROM ID Information Table

| Immobilizer | ECM P/NO. | ROM ID | Remark |
| --- | --- | --- | --- |
| Previous | New |
| ○ | 39103 - 2A710 | B0EHCM2EI02U C0EHCM2EI03U | C0EHCM2EI04T | Without Air Heater | High horsepower |
| 39103 - 2A715 | C0EHCM2EI04U C0EHCM2EI05U | C0EHCM2EI07U | With Air Heater |
| 39103 - 2A760 | B0ELCM2EI02U | C0ELCM2EI03T | Without Air Heater | Low horsepower |
| 39103 - 2A765 | C0ELCM2EI03U C0ELCM2EI04U | C0ELCM2EI06U | With Air Heater |

4. Operation Code And Time

■ Warranty Information

| OP CODE | OP NAME | OP TIME | NATURE | CAUSE |
| --- | --- | --- | --- | --- |
| 39110F48 | ECM UPGRADE | 0.2M/H | N13 | C40 |

N13: Poor acceleration, C40: Improper Adjustment

5. Service Procedure

■ NOTICE

1) Check if the battery is fully charged before upgrade.

2) Turn off all lamps (Do not leave head lamp switch in auto mode) and all accessories

(including heater, A/C, blower, radio, seat warmer, defogger, etc.) to make certain

the battery is not discharged during upgrade.

3) Perform the upgrade with the ignition key in the ON position.

4) Be careful not to disconnect any cables connected to the vehicle, Hi-Scan Pro or GDS during upgrade.

5) Do not start the engine during upgrade.

6) Do not turn off the ignition key during upgrade.

■ UPGRADE PROCEDURE

1. GDS ECM SOFTWARE UPGRADE PROCEDURE

1-1. GDS (GLOBAL DIAGNOSTIC SYSTEM) INSTALLATION PROCEDURE

A: Diagnostic terminal / B: VCI (Vehicle Communication Interface) / C: USB (Universal Serial Bus) cable D: DLC cable / E: Power supply cable

1) Connect the power supply connector to the diagnostic terminal.

NOTE)

- If attempting to perform the upgrade with the power supply cable disconnected from the diagnostic

terminal, make certain that the diagnostic terminal is fully charged before upgrade. If not, failure to

perform the upgrade may occur. Therefore, it is strongly recommended to connect the power supply

cable to the diagnostic terminal.

2) Connect the USB cable between the VCI and the diagnostic terminal.

NOTE)

- When performing the ECM upgrade using the GDS, wireless communication between the VCI and the

diagnostic terminal is NOT available. Therefore, be sure to connect the USB cable between the VCI and

the diagnostic terminal.

3) Connect the DLC cable from the VCI into the 16-pin data link connector (under the driver's side

instrument panel).

4) Turn on the VCI and diagnostic terminal with the ignition key in the ON position.

1-2. AUTOMATIC UPGRADE PROCEDURE USING GDS

1) Enter the vehicle information by entering the vehicle model, model year and selecting ENGINE as the

system.

2) Select ECM upgrade.

3) Select Auto Mode then ENGINE at the left ECM upgrade column.

4) Read preparations and touch OK.

5) After the current ROM ID is displayed, select Upgrade event, "65. ED 1.6 DIESEL HESITATION."

6) Upgrade will begin and progress of the upgrade will appear on the bar graph.

7) Upgrade will occur until 100% is indicated in the bar graph. Turn the ignition key OFF for 10 seconds,

place it back in the ON position and then select OK to continue according to information displayed on the

screen. Wait for the final screen, which indicates upgrade is complete.

8) Check for any engine or transmission section diagnostic trouble codes (DTCs) and erase any trouble

codes present.

9) Start the engine to confirm proper operation of the vehicle.

1-3. MANUAL UPGRADE PROCEDURE USING GDS

NOTE)

- The manual upgrade should be performed only when the automatic upgrade fails.

- If automatic upgrade fails, turn the ignition key OFF for about 10 seconds, place it back in the ON position

and then perform manual upgrade.

1) Within the ECM upgrade screen, select Manual Mode followed by ENGINE in the left column, then select

the Upgrade Event #65, appropriate ECM part number and OK.

2) Enter the correct password from the below table and then select OK.

| MENU | Password |
| --- | --- |
| 01. ED 1.6 VGT +IMMO: 39103 - 2A710 | 2710 |
| 02. ED 1.6 VGT +IMMO: 39103 - 2A715 | 2715 |
| 03. ED 1.6 VGT +IMMO: 39103 - 2A760 | 2760 |
| 04. ED 1.6 VGT +IMMO: 39103 - 2A765 | 2765 |

3) Upgrade will occur until 100% is indicated in the bar graph.

4) Turn the ignition key OFF for 10 seconds, place it back in the ON position and then select OK to continue

according to information displayed on the screen.

5) Wait for final screen, which indicates upgrade is completed.

6) Check for any engine or transmission section diagnostic trouble codes (DTCs) and erase any trouble

codes present.

7) Start the engine to confirm proper operation of the vehicle.

2. HI-SCAN PRO ECM SOFTWARE UPGRADE PROCEDURE

2-1. HI-SCAN PRO INSTALLATION PROCEDURE

| 1) Attach the CAN adapter (C) to the Hi-Scan Pro main body and securely tighten the two bolts. 2) Attach the Data Link Connector (DLC) cable (A) to the CAN adapter and securely tighten the two bolts. 3) Remove the system software card from the Hi-Scan Pro and insert the upgrade software card into the Hi-Scan Pro top slot (B). 4) Connect the DLC cable from the Hi-Scan Pro into the vehicle's connector (16-pin connector). |  |
| --- | --- |

2-2. AUTOMATIC UPGRADE PROCEDURE USING HI-SCAN PRO

1) Turn the ignition key to the ON position.

NOTE) Do not start the engine.

2) Turn on the Hi-Scan Pro and press ENTER.

| 3) Select option "65. ED 1.6 DIESEL HESITATION_2" and press ENTER. |  |
| --- | --- |

4) Select option "01. ED 1.6 DIESEL HESITATION_2 [AUTO]" and then press ENTER.

5) Enter "0525" as the password for automatic upgrade mode and press ENTER.

6) The Hi-Scan Pro will establish communication, check the ECM ROM ID and perform the upgrade.

NOTE)

- The Hi-Scan Pro detects the current ECM ROM ID, assigns the new ECM ROM ID and display them on the

Hi-Scan Pro screen.

- Check the ECM ROM IDs displayed on the Hi-Scan Pro screen to verify that the correct ECM software is

being downloaded. Refer to the "ROM ID information table" above.

- If the Hi-Scan Pro does not download the program, use the MANUAL UPGRADE PROCEDURE.

7) When "UPGRADE COMPLETED" message is displayed, turn off the Hi-Scan Pro.

8) Check if any incidental Diagnostic Trouble Codes (DTCs) have been created by the upgrade using the

Hi-Scan Pro with the system software card and clear the DTCs present.

9) Turn off the ignition key for 10 seconds and start the engine to confirm proper operation of the vehicle.

2-3. MANUAL UPGRADE PROCEDURE USING HI-SCAN PRO

NOTE)

- The manual upgrade should be performed only when the automatic upgrade fails.

1) Turn off the ignition key for 10 seconds and then place it back in the ON position.

2) Turn on the Hi-Scan Pro and press ENTER.

3) Select option "65. ED 1.6 DIESEL HESITATION_2" and press ENTER.

4) Select option "02. ED 1.6 DIESEL HESITATION_2 [ERROR]" and then press ENTER.

5) Select the appropriate vehicle type and press ENTER.

6) Enter the correct password from the following table and press ENTER.

| MENU | Password |
| --- | --- |
| 01. ED 1.6 VGT +IMMO: 39103 - 2A710 | 2710 |
| 02. ED 1.6 VGT +IMMO: 39103 - 2A715 | 2715 |
| 03. ED 1.6 VGT +IMMO: 39103 - 2A760 | 2760 |
| 04. ED 1.6 VGT +IMMO: 39103 - 2A765 | 2765 |

7) The Hi-Scan Pro will establish communication, check the ECM ROM ID and perform the upgrade.

NOTE)

- The Hi-Scan Pro detects the current ECM ROM ID, assigns the new ECM ROM ID and display them on the

Hi-Scan Pro screen.

- Check the ECM ROM IDs displayed on the Hi-Scan Pro screen to verify that the correct ECM software is

being downloaded. Refer to the "ROM ID information table" above.

8) When "UPGRADE COMPLETED" message is displayed, turn off the Hi-Scan Pro.

9) Check if any incidental Diagnostic Trouble Codes (DTCs) have been created by the upgrade using the

Hi-Scan Pro with the system software card and clear the DTCs present.

10) Turn off the ignition key for 10 seconds and start the engine to confirm proper operation of the vehicle.