| ; TSB ; . | Model; Cee'd [ED](); . |
| --- | --- |
| Group; Кузов (Интерьер и Экстерьер)(91); . |
| TSB No.; KFE08-91-V040-ED; . |
| Subject; . LEFT FRONT DOOR LATCH ASSEMBLY INSPECTION AND REPLACEMENT; . | Published; 1/30/2008; . |
| Area & Distributor; West Europe, East Europe; . |

1. Description

■  Symptom/Condition

On some cee’d (ED) vehicles, when locking all the doors by pushing the central door lock button and

pulling the door inside handle to open the driver’s door, the door inside handle may not operate.

■  Cause

Defective left front door latch assembly is applied.

■  Countermeasure

Inspect that the driver’s door inside handle operates normally. And, if necessary, replace the front left door

latch assembly with new one.

2. Applicable Vehicles;

■  Model : cee’d (ED)

■  Affected vehicle production date range: Produced from Nov. 23, 2007 to Nov. 30, 2007

■  Affected vehicle VIN range: See the file attached.

■  Area : Europe

3. Parts Information;

■ PARTS REQUIRED

| MODEL | PART NAME | PART NO. | FIGURE |
| --- | --- | --- | --- |
| cee’d & cee’d SW | Left front door latch assembly | 81310-1H000 |  |
| PRO_cee’d | Left front door latch assembly | 81310-1H300 |  |

Note)

This bulletin has been released after confirming parts availability from MOBIS Korea for your ordering reference. The actual supply of the mentioned part may take a month upon order.

4. Operation Code And Time

■ WARRANTY INFORMATION

| OP CODE | OPERATION | OP TIME | NATURE | CAUSE |
| --- | --- | --- | --- | --- |
| 81310F00 | LEFT FRONT door latch assembly inspection | 0.2 M/H | *N94 | **C28 |
| 81310F01 | LEFT FRONT door latch assembly INSPECTION AND Replacement | 0.7 M/H | *N94 | **C28 |

*N94 Inoperative

**C28 Poor welding

5. Service Procedure

| 1) Verify that the vehicle is an affected vehicle by identifying the VIN. |  |
| --- | --- |
| 2) Close all the doors from inside. |  |
| 3) Lock all the doors by pushing the central door lock button (A) |  |
| 4) Pull the driver’s door inside handle (B) from inside as quickly as possible. Note) The driver’s door should open at one try. |  |
| 5) Repeat step 4) 15 times. Note) If the driver’s door opens at one try, no further procedure is needed. But, if the driver’s door does not open, replace the left front door latch assembly with new one according to the applicable workshop manual. |  |