| ; TSB ; . | Model; Cee'd [ED](all), Optima/Magentis [MG] (all), Sportage [KM](all); . |
| --- | --- |
| Group; Механическая система двигателя(12); . |
| TSB No.; KGE08-12-P080-EDMGKM; . |
| Subject; . Caution during repair on CPF-equipped vehicles ; . | Published; 1/28/2008; . |
| Area & Distributor; Asia, Pacific, South America, C.America, West Europe, East Europe, Middle East, Africa; . |

1. Description

This bulletin provides information regarding caution during repair on the SPORTAGE (KM) 2.0L, OPTIMA (MG) 2.0L and cee'd (ED) 1.6L diesel vehicles equipped with Catalyzed Particulate Filters (CPF).

The CPF is a device designed to remove diesel particulate matter or soot from the exhaust gas by collecting the particulate and burning off the accumulated particulate.

If intake air leak occurs due to improperly tightened intercooler hose, it may cause damage to the CPF. Be sure to tighten the intercooler intake hose securely in place after carrying out the intercooler-related repair.

When the intercooler intake hose is NOT firmly held in place,

Intake air leak (Possible DTC : P0101, P0069, P2238)  → Insufficient amount of intake air → Rich air/fuel mixture and Increase in exhaust gas temperature → Excessive accumulation of soot in CPF → Damage to CPF during regeneration (Possible DTC : P2002), Deterioration of CPF's performance or Hard starting

| Normal condition | Improperly tightened intercooler hose |
| --- | --- |