|  | TECHNICAL SERVICE BULLETIN |
| --- | --- |

| TSB No. | KT2007030207 | TSB Type | Customer Care | Language | English |
| --- | --- | --- | --- | --- | --- |
| Distributor | 99604 (KMC) | Published | 3/2/2007 | Modified |  |
| Model | Cee'd(ED) (2007) |
| Area | West Europe<b |
| Group | Engine Electrical System |
| Subject | RETIGHTENING ALTERNATOR PULLEY MOUNTING NUT |

1. Description

This bulletin provides the procedure to retighten the alternator pulley mounting nut for cee’d

vehicles equipped with a Gamma engine.

■ Symptom/Condition

On some cee’d vehicles equipped with a Gamma engine, the alternator pulley mounting nut is not

tightened to the specified tightening torque.

■ Countermeasure/Remedy

Retighten the alternator pulley mounting nut to the specified tightening torque.

2. Vehicles Affected;

■ Model : cee’d vehicle equipped with Gamma engine

■ Affected vehicle production date range :

- Produced from Nov. 13, 2006.11.13 to Dec. 11, 2006

■ Affected vehicle VIN range : Produced from U5YFF24127L001023 to U5YFF24227L001500

■ Area : Europe

3. Parts Information;

■ PARTS REQUIRED

- Tools required

| Tool name | Usage | Figure |
| --- | --- | --- |
| Alternator pulley nut socket wrench | Removal of alternator pulley |  |
| Alternator pulley holder | Holding alternator pulley when fastening or unfastening alternator pulley nut |  |

4. Operation Code And Time

| OP CODE | OPERATION | OP TIME | NATURE | CAUSE |
| --- | --- | --- | --- | --- |
| 070S05A0 | RETIGHTENING ALTERNATOR PULLEY NUT | 0.2 M/H | N86 | C27 |

*N86 : Loosening

**C27 : Insufficient tightening

5. Service Procedure

| 1. Verify that the vehicle is affected one. 2. Fit the alternator pulley mounting nut socket wrench (B) onto the pulley mounting nut (A). 3. Pass the alternator pulley holder (C) through the below of engine mounting bracket (D) and assemble it(C) with the socket wrench (B). 4. Assemble a torque wrench (E) with the socket wrench (B). |  |
| --- | --- |
| 5. Tighten the alternator pulley mounting nut to the specified tightening torque by using a torque wrench. - Tightening torque: 8.5~9.5 Kgf.m(83.4~93.2 N.m, 61.5~68.7 lbf.ft ) |  |
| Caution) 1) When tightening the nut, be slow to increase force to secure the specified tightening torque of the nut. 2) Be careful not to damage the drive belt and the neighborhood parts. |  |